Espoo Bricks

## Espoo M0002 Brick
### Module overview
Espoo M0002 Brick is an electronic WiFi module designed to operate the DS18B20 sensor. The module was built based on the ESP8266 chipset.
The module features:
- WiFi interface
- programming interface
- connector for DS18B20 sensor
- universal button
- programmable LED
- power indicator LED
The module can be programmed using the Arduino environment.
### Hardware
#### Pinout

- DS18B20 DQ is connected to GPIO4 pin
- switch is connected to GPIO0 pin
- buildin LED is connected to GPIO2 pin
#### Circuit diagram

### Programming Espoo M0002 Brick with Arduino
#### Led blinking
Sample arduino program for Espoo M0002 module blinking the built-in LED. The LED is connected to GPIO2 pin.

#### Switch operation
Sample Arduino program for Espoo M0002 module, illuminating the built-in LED when the button is pressed. The button is connected to GPIO0 pin, and the LED is connected to GPIO2 pin.

#### DS18B20 temperature read
Below is the Arduino program that reads temperature from the DS18B20 sensor using the Espoo M0002 module. The temperature is displayed on the console. The sensor is connected to GPIO4 pin. To run the program, you need to install two libraries, OneWire and DallasTemperature and set SerialMonitor speed to 9600b/s.

Install OneWire library:

Install DallasTemaperature library:

Run DS18B20 program on Espoo M0002 brick:

#### WiFi Acces Point