Espoo Bricks

## Espoo M0002 Brick
### Module overview
Espoo M0002 Brick is an electronic WiFi module designed to operate the DS18B20 sensor. The module was built based on the ESP8266 chipset.
The module features:
- WiFi interface
- programming interface
- connector for DS18B20 sensor
- universal button
- programmable LED
- power indicator LED
The module can be programmed using the Arduino environment.
### Hardware
#### Pinout

- DS18B20 DQ is connected to GPIO4 pin
- switch is connected to GPIO0 pin
- buildin LED is connected to GPIO2 pin
#### Circuit diagram

### Programming Espoo M0002 Brick with Arduino
#### Led blinking
Sample arduino program for Espoo M0002 module blinking the built-in LED. The LED is connected to GPIO2 pin.

#### Switch operation
Sample Arduino program for Espoo M0002 module, illuminating the built-in LED when the button is pressed. The button is connected to GPIO0 pin, and the LED is connected to GPIO2 pin.

#### DS18B20 temperature read

#### WiFi Acces Point